Evaluating effects of memory compressed usage on MeeGo

---
Agenda

---
Why compressed memory?
  - Generally, memory is scarce.
  - Hardware changes bring more co$ts.
  - A software solution can relief the memory scarcity.
  - Flash storage suffers from wear-leveling issues, so its useful if we can avoid using them as swap device

---
Related work
  - 1993 – Douglis with first comp. cache implementation.
  - 1999 – Kaplan with new adaptive scheme.
  - Following the same scheme, Rodrigo Castro released an implementation with new compressed storage structures approach and new adaptive re-sizing approach. It was for 2.4.x Linux kernel.
  - CRAMES – Compressed RAM for Embedded Systems.

---
Compcache: previous version
  - Changes to the swap write path, page fault handler and page cache lookup functions.
  - Intrusive nature.

---
Compcache: ramzswap module
  - RAM based block device used as swap disk.
  - Swapped pages are compressed and stored in memory itself.
  - Requested pages are decompressed before swapped-out.

---
Compcache: implementation
  - Far less intrusive than previous approach.
  - Do not compress page cache (filesystem backed) pages.
  - Compress anonymous pages only.
  - Individual components:
    - LZO compressor.
    - xvMalloc memory allocator.
    - compcache block device driver: ramzswap.
  - swapon /dev/ramzswap0

---
Compcache: memory management
  - How manage the variable size of the compressed chunks?
  - How reduce the fragmentation?

---
Compcache: memory management
  - xvMalloc: O(1) malloc/free.
  - Very low fragmentation as presented on all tests.
  - Can use highmem.
  - Non-standard allocator interface.

---
Compcache: limitations
  - ramzswap can never know when a compressed page is no longer required.
  - Swap discard mechanism: BIO_RW_DISCARD
  - If there is no swap operations the stale pages will remain.
  - ramzswap can simply forward uncompressible pages to a backing swap disk, but it cannot swap out memory allocated by xvmalloc.

---
Tests platforms
  - N9 + Harmattan
    - has ramzswap as default swap device: ~ 256 MB
    - Swappiness = 30
    - RAM 1GB
  - N900 running MeeGo by Community
    - has MMC block device as default swap device: ~ 75 MB
    - RAM 128 MB
  - Tests consists in memory allocation speed (fillmem, scan utilities), and low memory situations: multiple applications running.

---
Compcache experiments
  - Is ramzswap overhead affecting memory allocation speed?
  - Is ramzswap enabling other use cases when memory consumption is critical?

---
N9 experiments
- Performance tests
  - Memory allocation speed
- Memory consumption
  - Memory behavior when applications are running and ramzswap is being used or not

---
N9 experiments
  - Performance: Time to allocate 550 MB
No ramzswap
Default conf
Swappiness = 60
Time (s)

---
N9 experiments
Compressed memory after 550 MB allocated

---
N9 experiments
- Memory consumption
  - 8 browsers instances
  - Calendar
  - Video player
  - Music player

---
N9 experiments
Memory consumption behavior: MemFree

---
N9 experiments
Ramzswap stats
Default configuration
Swappiness = 60
DiskSize:	262144 kB
NumReads:	648
NumWrites:	2183
FailedReads:	0
FailedWrites:	0
InvalidIO:	0
NotifyFree:	0
ZeroPages:	68
GoodCompress:	87 %
NoCompress:	1 %
PagesStored:	2115
PagesUsed:	502
OrigDataSize:	8460 kB
ComprDataSize:	1979 kB
MemUsedTotal:	2008 kB
DiskSize:	262144 kB
NumReads:	897
NumWrites:	10576
FailedReads:	0
FailedWrites:	0
InvalidIO:	0
NotifyFree:	0
ZeroPages:	419
GoodCompress:	76 %
NoCompress:	5 %
PagesStored:	10157
PagesUsed:	3206
OrigDataSize:	40628 kB
ComprDataSize:	12682 kB
MemUsedTotal:	12824 kB

---
N9 experiments
Ramzswap stats
Default configuration
Swappiness = 60
DiskSize:	262144 kB
NumReads:	648
NumWrites:	2183
FailedReads:	0
FailedWrites:	0
InvalidIO:	0
NotifyFree:	0
ZeroPages:	68
GoodCompress:	87 %
NoCompress:	1 %
PagesStored:	2115
PagesUsed:	502
OrigDataSize:	8460 kB
ComprDataSize:	1979 kB
MemUsedTotal:	2008 kB
DiskSize:	262144 kB
NumReads:	897
NumWrites:	10576
FailedReads:	0
FailedWrites:	0
InvalidIO:	0
NotifyFree:	0
ZeroPages:	419
GoodCompress:	76 %
NoCompress:	5 %
PagesStored:	10157
PagesUsed:	3206
OrigDataSize:	40628 kB
ComprDataSize:	12682 kB
MemUsedTotal:	12824 kB

---
N9 experiments
- Memory consumption
  - Default configuration
    - Good responsiveness but the video did not play.
  - No swap
    - After the six browser instance the responsiveness was decreasing and the video player did not start.
  - With ramzswap
    - Responsiveness ok, all applications started and worked properly.

---
N900 tests
  - Performance

---
N900 tests
  - Memory consumption